## Slide 1: Internet of Things (IoT)
Chapter 2
IoT Architecture
“We must have life-building, man-making, character-making assimilation of ideas.” – Swami Vivekananda
Course Code: CSE0612405

## Slide 2: What is Architectural Plan?
In present days, networks
run the modern business
So, it should never be built
without careful planning
Smart Home
Architecture is how you design your application or solution.
Essence of IoT architecture:
  how the data is
    transported,
    collected,
    analyzed, and
    ultimately acted upon.
Driving forces:
Scale
Security
Constrained devices
Massive data
Data analysis
Support to legacy devices

## Slide 3: Basic 3-Layer architecture
Perception layer is the physical layer, which has sensors for sensing and gathering information about the environment.
Network layer is responsible for connecting to other smart things, network devices, and servers. Its features are also used for transmitting and processing sensor data.
Application layer is responsible for delivering application specific services to the user.
– For example, smart homes, smart
cities, smart health, etc.
Source: https://www.pinterest.com/pin/641129696942354756/

## Slide 4: Commonly used 4-Layer architecture
Sensing layer: This layer includes sensors and actuators that are placed in the environment to gather information
Network layer: It includes protocols and technologies that enable devices to connect and communicate with each other and with the wider internet.
Data processing Layer: It includes a variety of technologies and tools, such as data management systems, analytics platforms, and machine learning algorithms, to extract meaningful insights from the data and make decisions based on that data.
Application Layer: It includes various software and applications such as mobile apps, web portals, and other user interfaces that are designed to interact with the underlying IoT infrastructure.
Source: Sikder et al., “A Survey on Sensor-based Threats to Internet-of-Things (IoT) Devices and Applications” IEEE Communications Surveys & Tutorials, 23(2), pp. 1125 - 1159, 2021.

## Slide 5: Emergence of Standard IoT Architecture
However, the basic 3-layer or commonly used 4-layer architectures did not address many issues.
In fact, IoT did not have any standard defined architecture of working which is strictly followed universally.
Few Existing Issues:
  Highly fragmented marked with limited vendor-
specific applications
  Each application vertical contains its own technologies without interoperability
  Incompatibility for seamless integration between
heterogeneous applications and devices
  Did not consider security aspect in design
So, in the past several years, few architectural standards and frameworks have emerged
Two best-known architectures:
  oneM2M architecture
  IoT World Forum architecture
Source: https://onem2m.org/using-onem2m/developers/basics
5

## Slide 6: oneM2M Architecture
Challenges in IoT Architecture:
heterogeneity of devices,
heterogeneity of software,
Heterogeneity of access methods
Using the smart building use case, a security application can detect when nobody is in the building.
It could then trigger lights to be switched off and for the HVAC system to operate on a reduced
setting.
Image Source: https://onem2m.org/using-onem2m/developers/basics
Goal of oneM2M architecture:
to create a common services layer, which can be readily embedded in field devices to allow communication with application servers.

## Slide 7: oneM2M Architecture
Proposed by Européen Télécommunications Standards Institute (ETSI)
oneM2M architecture divides IoT functions into three major domains.
First
  Defines application-layer protocols
  Attempts to standardize northbound API
API (Application Programming Interface)
Note: Interface can be thought of as a contract of service between two applications or parties. This contract defines how the two communicate with each other using requests and responses.
  A northbound interface allows a particular component of a network to communicate with a higher-level component.
  Applications have their own sets of data models

## Slide 8: oneM2M Architecture
Proposed by Européen Télécommunications Standards Institute (ETSI)
oneM2M architecture divides IoT functions into three major domains.
First Second
  horizontal framework across the vertical industry applications.
  Include:
    the physical network that the IoT applications run on. (e.g. backhaul network)
    the underlying management protocols
    the hardware
cont…

## Slide 9: oneM2M Architecture
Proposed by European Telecommunications Standards Institute (ETSI)
oneM2M architecture divides IoT functions into three major domains.
top is the common services layer
This layer adds APIs and middleware supporting third-party services and applications.
Service layer can be readily embedded within various hardware and software nodes
A RESTful API uses HTTP requests to GET, PUT, POST and DELETE data.
First Second

## Slide 10: oneM2M Architecture
Proposed by European Telecommunications Standards Institute (ETSI)
oneM2M architecture divides IoT functions into three major domains.
First Second Third
IoT devices, & communication network (802.15.4, LoRa,
WiFi)

## Slide 11: IoTWF Architecture – 7 Layer Stack
IoTWF architectural committee (led by Cisco, IBM, Rockwell Automation, and others) aims to -
offers a clean, simplified perspective on IoT
includes edge computing, data storage, and data access
concise way of visualizing IoT from a technical perspective
  Decompose the IoT problem into smaller parts
  Identify different technologies
at each layer
  Different parts of a system can be provided by different vendors
  Tiered security model enforced at the transition points between levels
  Define interfaces that leads to
interoperability

## Slide 12: Layers 1 & 2
Layer 1: Physical Devices and Controllers Layer
home of the “things” in IoT
“things” can be from a microscopic sensors to giant machines in a factory
primary function is generating data
capable of being queried and/or controlled over a network.
Layer 2: Connectivity Layer
focus is on connectivity

## Slide 13: Layer 3 : Fog Layer
Basic principle:
information processing is initiated as early and as close to the edge of the network as possible.
Layer 3: Edge Computing Layer
often referred to as the “fog” layer
emphasis is on
  Data reduction by filtering and cleaning up
  Reformatting and compressing data
  Initial processing of data (e.g. alert generation, data validation, etc)

## Slide 14: Upper Layers: Layers 4–7
Layers | Functions
Layer 4: Data Accumulation | Captures data and stores it for applications Convert event-based data to query-based processing
Layer 5: Data Abstraction | Reconciles multiple data formats Ensures consistent semantics for various data sources Confirmation about dataset completeness
Layer 6: Application | Interpret data using software applications Applications may monitor, control, and provide report based on analysing the data
Layer 7: Collaboration and processes | Consumes and shares the application information Collaborating and communicating IoT information

## Slide 15: Unified IoT Architecture
It highlights the fundamental building blocks that are common to most IoT systems and which is intended to help in designing an IoT network.
IoT architectural framework is presented as two parallel stacks
  Core IoT Functional Stack
  IoT Data Management and Compute Stack

## Slide 16: Lessons Learned
What is the need of IoT architecture?
3-Layer and 4-Layer IoT Architectures
About oneM2M architecture
About IoT WF architecture
Unified IoT Architecture

## Slide 17
Figures and slide materials are taken from the following sources:
1. David Hanes et al., “IoT Fundamentals: Networking Technologies, Protocols, and Use Cases for the Internet of Things”, 1st Edition, 2018, Pearson India.